## Slide 1
COMPUTER ORGANIZATION AND ARCHITECTURE
Computer Arithmetic
DESIGNING FOR PERFORMANCE
11th Edition, Global Edition
William Stallings
CHAPTER 11

## Slide 2
SLIDE 2
1. ALU & Integers
ALU block diagram, Integer representation systems (Sign-Magnitude, Twos Complement, Biased representation), and sign extension rules.
2. Integer Arithmetic
Logic gates negation, subtraction overflow checks, high-performance Booth's multiplication algorithm, and division mechanics.
3. FP Representation
Scientific notations, standard IEEE 754 layouts (binary32, binary64, binary128 formats), and handling edge states.
4. FP Arithmetic
Complex calculations, rounding constraints, guard bits, strict interval computations, and handling extreme NaNs.
TABLE OF CONTENTS

## Slide 3
SLIDE 3
The central core of the computer processing system that performs all mathematical calculations and logical evaluations.
Every other computational element is designed to fetch, move, or store data operands for the ALU to execute.
Constructed completely out of binary digital logic structures that evaluate basic Boolean algebra rules.
✦
✦
✦
ARITHMETIC & LOGIC UNIT (ALU)

## Slide 4
SLIDE 4
Decimal & Standard Notations
Human arithmetic systems leverage specialized conceptual abstractions for arithmetic, including:
Hardware Level Constraints
Digital memory cells and computational registers have physical constraints:
Explicit signs for negative integers
Radix points to denote fractions
No special symbols allowed for minus signs
Only absolute 1s and 0s are used
✦
✦
✦
✦
INTEGER REPRESENTATION

## Slide 5
Table 11.1: Standard Architectural Rules of Twos Complement
SLIDE 5
Characteristic | Definition / Standard Operational Rule
Representational Range | -2n-1 up to 2n-1 - 1
Representations of Zero | One unique representation (0000...0000)
Negation Rule | Invert each individual bit (Boolean complement), then add 1.
Bit Extension | Move the sign bit left and pad new bits with original sign state.
Addition Overflow Rule | Overflow occurs if and only if two inputs of matching signs produce an output with the opposite sign.
Subtraction Rule | Complement the subtrahend and perform standard addition: A - B = A + (-B).
TWOS COMPLEMENT CHARACTERISTICS

## Slide 6
Table 11.2: Comparative Systems for 4-Bit Layouts
SLIDE 6
Decimal | Sign-Magnitude | Twos Complement | Biased (Bias = 8)
+8 | – | – | 1111
+7 | 0111 | 0111 | 1110
+4 | 0100 | 0100 | 1011
+1 | 0001 | 0001 | 1000
+0 / -0 | 0000 / 1000 | 0000 | 0111
-1 | 1001 | 1111 | 0110
-4 | 1100 | 1100 | 0011
-8 | – | 1000 | 0000
ALTERNATIVE 4-BIT INTEGERS

## Slide 7
SLIDE 7
Sign-Magnitude Limits
Accomplished by shifting the sign bit to the absolute leftmost position and padding the intermediary spaces with zeros.
Twos Complement Rule
Shift the sign bit to the leftmost slot and pad remaining intermediary bits with a copy of the sign bit.
Positive numbers: Pad left spaces with zeros
Negative numbers: Pad left spaces with ones
RANGE EXTENSION & SIGN EXTENSION

## Slide 8
SLIDE 8
Twos Complement Logic:
Compute the bitwise Boolean inversion of every single bit of the input word.
Add 1 to the resulting bit pattern, evaluating it as an unsigned value.
This double-inversion loop naturally proves that the negation of a negated value resolves back to the original value.
Example conversion of +18 to -18 and back:
✦
✦
✦
FIXED-POINT NEGATION

## Slide 9
SLIDE 9
Case 1: Zero (0)
Case 2: Minimal Negative
Zero complements back to itself:
(Carry out/overflow is ignored; -0 = 0)
The asymmetric floor limits negation:
The MSB fails to invert! Standard overflow flag triggers to flag this arithmetic limitation.
NEGATION SPECIAL CASES

## Slide 10
SLIDE 10
Standard Addition Rule
Perform direct binary addition bitwise. Monitor signs of inputs and outputs:
Hardware Subtraction
Rather than using distinct arithmetic structures, compute negative complement and add:
A - B = A + TwosComplement(B)
If opposite signs are added, overflow is physically impossible.
If identical signs are added and the result sign flips, overflow occurred.
✦
✦
ADDITION & SUBTRACTION

## Slide 11
SLIDE 11
Evaluated by calculating intermediate partial products for each non-zero position in the multiplier factor.
Each step yields either all zeros or a shifted copy of the multiplicand.
Final product resolves by performing successive accumulation of all generated partial product steps.
✦
✦
✦
UNSIGNED MULTIPLICATION

## Slide 12
SLIDE 12
Decision Operations
A powerful technique that accelerates signed multiplication. Operates on adjacent bits Q0 and Q-1:
Arithmetic Shifting
During the subsequent shift step, a crucial shift must execute to preserve correctness:
Arithmetic right shift is strictly required instead of logical right shift to correctly preserve the negative sign bit.
01: Add M to high half of product
10: Subtract M from high half of product
00 / 11: No arithmetic operation needed
✦
✦
✦
BOOTH'S ALGORITHM

## Slide 13
SLIDE 13
Closely mirrors standard long-hand division logic practiced in manual base-10 algebra.
Progresses by evaluating intermediate subtractions to confirm whether the divisor word matches inside the current partial remainder.
Resolves by appending a '1' bit into the quotient if subtraction completes, or a '0' if remainder check fails.
✦
✦
✦
UNSIGNED DIVISION

## Slide 14
SLIDE 14
Dynamic Scientific Strategy
By defining a dynamic, sliding binary radix point, floating-point representations enable a significantly expanded numeric scale.
A given floating-point value is standardly parameterized as:
Significand × Base Exponent
Fixed-Point Limitations
Fixed-point registers face structural scaling constraints:
Cannot express huge scientific values
Cannot preserve extremely minute fractions
✦
✦
FLOATING-POINT PRINCIPLES

## Slide 15
SLIDE 15
Arithmetic Format
Fully defined operations which standard-compliant processors must evaluate directly on hardware pathways.
Basic Format
Covers 5 core configurations (3 binary and 2 decimal) specifying layout bit allocations required for standard mathematical tools.
Interchange Format
Specifies bit-exact layouts for consistent file transfers, protecting data integrity when migrating files between architectures.
IEEE STANDARD 754 FORMATS

## Slide 16
Table 11.3: IEEE Standard Bit Allocation Schemes
SLIDE 16
Parameter | Binary32 (Single) | Binary64 (Double) | Binary128 (Quadruple)
Storage Width (bits) | 32 | 64 | 128
Exponent Width (bits) | 8 | 11 | 15
Exponent Bias | 127 | 1023 | 16383
Trailing Significand (bits) | 23 | 52 | 112
Smallest Positive Normal |  |  | 
Largest Positive Normal | ~ | ~ | ~
Parameter | Binary32 (Single) | Binary64 (Double) | Binary128 (Quadruple)
Storage Width (bits) | 32 | 64 | 128
Exponent Width (bits) | 8 | 11 | 15
Exponent Bias | 127 | 1023 | 16383
Trailing Significand (bits) | 23 | 52 | 112
Smallest Positive Normal |  |  | 
Largest Positive Normal |  |  | 
IEEE 754 FORMAT PARAMETERS

## Slide 17
SLIDE 17
Extended Formats
Adds extra bits directly to exponent fields and significand words to prevent computation degradation:
Extendable Formats
Provides complete programmatic control over bit lengths to evaluate critical custom scientific steps:
Protects intermediate operations from accumulative roundoff.
Avoids spurious overflows in intermediate calculations.
Tailors numeric precision parameters programmatically.
Offers custom flexibility for high-end modeling fields.
✦
✦
✦
✦
EXTENDED & EXTENDABLE PRECISION

## Slide 18
Table 11.5: Word Interpretations for Standard binary32
SLIDE 18
Sign | Biased Exponent | Fraction Field | Interpreted Value
0 / 1 | 0 | 0 | Positive / Negative Zero
0 / 1 | all 1s | 0 | Plus / Minus Infinity (∞)
0 or 1 | all 1s | ≠ 0 (MSB = 1) | Quiet NaN (qNaN)
0 or 1 | all 1s | ≠ 0 (MSB = 0) | Signaling NaN (sNaN)
0 | 0 < e < 255 | f | 2e-127(1.f) [Positive Normal]
1 | 0 < e < 255 | f | -2e-127(1.f) [Negative Normal]
0 / 1 | 0 | f ≠ 0 | ± 2-126(0.f) [Subnormal]
IEEE 754 WORD INTERPRETATIONS

## Slide 19
SLIDE 19
Mathematical Formulas
Floating-point operations align to the following structures (given XE ≤ YE):
Calculation Trace
Evaluating: X = 0.3 × 102, Y = 0.2 × 103
Addition: (XS × BXE - YE + YS) × BYE
Subtraction: (XS × BXE - YE - YS) × BYE
Multiplication: (XS × YS) × BXE + YE
Division: (XS ÷ YS) × BXE - YE
X + Y = (0.3 × 102-3 + 0.2) × 103
= (0.03 + 0.2) × 103
= 0.23 × 103 = 230
FP ARITHMETIC OPERATIONS

## Slide 20
SLIDE 20
Guard Bits Strategy
Guard bits are extra temporary registers configured to the right of intermediate fractions during arithmetic steps.
They prevent massive precision drop-offs when evaluating subtractions of highly similar numbers.
IEEE Rounding Standard
Round to Nearest: Rounds to matching even value in ties.
Round toward +∞: Rounds upward to positive values.
Round toward -∞: Rounds downward to negative values.
Round toward 0: Truncates all remaining fractional elements.
✦
✦
✦
✦
PRECISION & GUARD BITS

## Slide 21
SLIDE 21
Interval Boundary Computations
Produces upper and lower bounds containing the true, exact real result to help trace calculation limits:
Truncation Disadvantages
Simplest rounding technique where extra bits are completely discarded (round toward zero):
While simple, this method introduces persistent, biased rounding error toward zero.
Width of output interval indicates propagation of error.
Extremely useful in scientific computing.
✦
✦
INTERVAL ARITHMETIC

## Slide 22
SLIDE 22
Infinity Evaluations
Treated as standard algebraic limit values in real calculations:
Table 11.7: Quiet NaN Triggers
Quiet NaNs generate on undefined mathematical operations:
5 + (+∞) = +∞
5 ÷ (+∞) = +0
(+∞) + (+∞) = +∞
(-∞) - (+∞) = -∞
Magnitude subtraction of infinities: (∞ - ∞)
Invalid multiplications: 0 × ∞
Invalid divisions: 0 ÷ 0 or ∞ ÷ ∞
Negative square roots: √x where x < 0
SPECIAL MATHEMATICAL STATES

## Slide 23
SLIDE 23
Logic Core & ALU: Arithmetic operations evaluate on binary digital structures.
Signed Representation: Twos complement solves sign issues with one unique zero representation.
Booth's Multiplication: Accelerates signed multiplication using arithmetic shifts.
IEEE 754 Standard: Provides strict rules across single, double, and quad precision layouts.
✦
✦
✦
✦
CHAPTER 11 SUMMARY

## Slide 24
SLIDE 23
CHAPTER 11 SUMMARY
Question 1: In twos complement representation, which of the following operations is used to perform the negation of an integer?
A. Invert only the value of the sign bit (the leftmost bit).
B. Take the Boolean complement (bit inversion) of each binary bit, then add 1 to the result.
C. Perform an arithmetic right shift to preserve the sign bit.
D. Perform sign extension by filling the left side with 0 bits.
Answer: B

## Slide 25
SLIDE 23
CHAPTER 11 SUMMARY
Question 2: According to the IEEE 754 standard for floating-point representation, a number stored in a binary word consists of which three fields?
A. Sign bit, Base, and Significand.
B. Sign bit, Exponent, and Significand.
C. Exponent, Significand, and Guard bit.
D. Sign bit, Significand, and Implicit bit.
Answer: B

## Slide 26
SLIDE 24
Questions & Answers
We have completed the review of Chapter 11 from the standard 11th Edition Global presentation of **"Computer Organization and Architecture"** (William Stallings).
Chapter 11 Review Hardware Arithmetic